Wireless communication between nodes using DSR Protocol

dsr.tcl
# ======================================================================
# Define options
# ======================================================================
set val(chan) Channel/WirelessChannel ;# channel type
set val(prop) Propagation/TwoRayGround ;# radio-propagation model
set val(netif) Phy/WirelessPhy ;# network interface type
set val(mac) Mac/802_11 ;# MAC type
set val(ifq) Queue/DropTail/PriQueue ;# interface queue type
set val(ll) LL ;# link layer type
set val(ant) Antenna/OmniAntenna ;# antenna model
set val(ifqlen) 50 ;# max packet in ifq
set val(nn) 3 ;# number of mobilenodes
set val(rp) DSR ;# routing protocol
set val(x) 500 ;
set val(y) 400 ;
set val(stop) 150 ;

set ns [new Simulator]
#Creating trace file and nam file
set tracefd [open dsr.tr w]
set windowVsTime2 [open win.tr w]
set namtrace [open dsr.nam w]

$ns trace-all $tracefd
$ns namtrace-all-wireless $namtrace $val(x) $val(y)

# set up topography object
set topo [new Topography]

$topo load_flatgrid $val(x) $val(y)

create-god $val(nn)

# configure the nodes
        $ns node-config -adhocRouting $val(rp) \
        -llType $val(ll) \
        -macType $val(mac) \
        -ifqType $val(ifq) \
        -ifqLen $val(ifqlen) \
        -antType $val(ant) \
        -propType $val(prop) \
        -phyType $val(netif) \
        -channelType $val(chan) \
        -topoInstance $topo \
        -agentTrace ON \
        -routerTrace ON \
        -macTrace OFF \
        -movementTrace ON

      for {set i 0} {$i < $val(nn) } { incr i } {
        set node_($i) [$ns node]
      }

# Provide initial location of mobilenodes
$node_(0) set X_ 5.0
$node_(0) set Y_ 5.0
$node_(0) set Z_ 0.0

$node_(1) set X_ 490.0
$node_(1) set Y_ 285.0
$node_(1) set Z_ 0.0

$node_(2) set X_ 150.0
$node_(2) set Y_ 240.0
$node_(2) set Z_ 0.0

# Generation of movements
$ns at 10.0 "$node_(0) setdest 250.0 250.0 3.0"
$ns at 15.0 "$node_(1) setdest 45.0 285.0 5.0"
$ns at 110.0 "$node_(0) setdest 480.0 300.0 5.0"

# Set a TCP connection between node_(0) and node_(1)
set tcp [new Agent/TCP/Newreno]
$tcp set class_ 2
set sink [new Agent/TCPSink]
$ns attach-agent $node_(0) $tcp
$ns attach-agent $node_(1) $sink
$ns connect $tcp $sink
set ftp [new Application/FTP]
$ftp attach-agent $tcp
$ns at 10.0 "$ftp start"

# Printing the window size
proc plotWindow {tcpSource file} {
global ns
set time 0.01
set now [$ns now]
set cwnd [$tcpSource set cwnd_]
puts $file "$now $cwnd"
$ns at [expr $now+$time] "plotWindow $tcpSource $file" }
$ns at 10.1 "plotWindow $tcp $windowVsTime2"

# Define node initial position in nam
for {set i 0} {$i < $val(nn)} { incr i } {
# 30 defines the node size for nam
$ns initial_node_pos $node_($i) 30
}

# Telling nodes when the simulation ends
for {set i 0} {$i < $val(nn) } { incr i } {
    $ns at $val(stop) "$node_($i) reset";
}

# ending nam and the simulation
$ns at $val(stop) "$ns nam-end-wireless $val(stop)"
$ns at $val(stop) "stop"
$ns at 150.01 "puts \"end simulation\" ; $ns halt"
proc stop {} {
    global ns tracefd namtrace
    $ns flush-trace
    close $tracefd
    close $namtrace
exec nam dsr.nam &
exit 0
}

$ns run

Output:

fcrit@FCRIT:~/Downloads$ ns dsr.tcl
num_nodes is set 3
warning: Please use -channel as shown in tcl/ex/wireless-mitf.tcl
INITIALIZE THE LIST xListHead
channel.cc:sendUp - Calc highestAntennaZ_ and distCST_
highestAntennaZ_ = 1.5, distCST_ = 550.0
SORTING LISTS ...DONE!
Segmentation fault (core dumped)
fcrit@FCRIT:~/Downloads$ nam dsr.nam