MAC Contention Window Wireless Network
# ======================================================================
# Define options
# ======================================================================
set val(chan) Channel/WirelessChannel ;# channel type
set val(prop) Propagation/TwoRayGround ;# radio-propagation model
set val(netif) Phy/WirelessPhy ;# network interface type
set val(mac) Mac/802_11 ;# MAC type
set val(ifq) Queue/DropTail/PriQueue ;# interface queue type
set val(ll) LL ;# link layer type
set val(ant) Antenna/OmniAntenna ;# antenna model
set val(ifqlen) 50 ;# max packet in ifq
set val(nn) 25 ;# default number of mobilenodes
set val(rp) AODV ;# routing protocol
set val(sc)	"./scenario"	;# scenario file
set val(x)	150.0	;
set val(y)	150.0	;
set val(simtime)	25.0	; #sim time
set val(rlen)	5	;
# ======================================================================
# Main Program
# ======================================================================

if { $argc != 2 } {
        puts "Wrong no. of cmdline args."
puts "Usage: ns cwsim.tcl -rlen <rlen>"
        exit 0
}

proc getopt {argc argv} {
        global val
        lappend optlist rlen

        for {set i 0} {$i < $argc} {incr i} {
        set arg [lindex $argv $i]
        if {[string range $arg 0 0] != "-"} continue
        set name [string range $arg 1 end]
        set val($name) [lindex $argv [expr $i+1]]
        }

set val(nn) [expr $val(rlen) * $val(rlen)]

}

getopt $argc $argv
#
# Initialize Global Variables
#
set ns_	[new Simulator]
set tracefd [open cwsim.tr w]
$ns_ trace-all $tracefd

set namtrace [open cwsim.nam w] ;# for nam tracing
$ns_ namtrace-all-wireless $namtrace $val(x) $val(y)
$ns_ use-newtrace

# set up topography object
set topo [new Topography]

$topo load_flatgrid $val(x) $val(y)

#
# Create God
#

set god_ [ create-god $val(nn) ]

$val(mac) set bandwidth_ 22.0e6
$val(mac) set CWMin_ 31
$val(mac) set CWMax_ 31

#
# Create the specified number of mobilenodes [$val(nn)] and "attach" them
# to the channel.

# configure node

        $ns_ node-config -adhocRouting $val(rp) \
-llType $val(ll) \
-macType $val(mac) \
-ifqType $val(ifq) \
-ifqLen $val(ifqlen) \
-antType $val(ant) \
-propType $val(prop) \
-phyType $val(netif) \
-channelType $val(chan) \
-topoInstance $topo \
-agentTrace ON \
-routerTrace OFF \
-macTrace ON \
-movementTrace OFF

for {set i 0} {$i < $val(nn) } {incr i} {
set node_($i) [$ns_ node]
$node_($i) random-motion 0	;# disable random motion
}

#
# Provide initial (X,Y, Z=0) co-ordinates for mobilenodes
#

set gridspace [expr 150.0 / $val(rlen)]

for {set i 0} {$i < $val(rlen) } {incr i} {
for {set j 0} {$j < $val(rlen) } {incr j} {
set a [expr $j + [expr $i * $val(rlen)]]
$node_($a) set X_ [expr 0.0 + [ expr $i * $gridspace]]
$node_($a) set Y_ [expr 0.0 + [ expr $j * $gridspace]]
$node_($i) set Z_ 0.0
}
}

# Define node initial position in nam

for {set i 0} {$i < $val(nn)} {incr i} {

    # 20 defines the node size in nam, must adjust it according to your scenario
    # The function must be called after mobility model is defined

    $ns_ initial_node_pos $node_($i) 20

set udp_($i) [new Agent/UDP]
$ns_ attach-agent $node_($i) $udp_($i)

set cbr_($i) [new Application/Traffic/CBR]
$cbr_($i) set packetSize_ 512
$udp_($i) set packetSize_ 512
$cbr_($i) set interval_ 0.01
$cbr_($i) set random_ 0.348
$cbr_($i) set maxpkts_ 1000000
$cbr_($i) attach-agent $udp_($i)

set null_($i) [new Agent/Null]
$ns_ attach-agent $node_($i) $null_($i)

}

#
# Tell nodes when the simulation ends
#
for {set i 0} {$i < $val(nn) } {incr i} {

    set dst [expr [expr $i + $val(rlen)] % $val(nn)]
    $ns_ connect $udp_($i) $null_($dst)
    $ns_ at [expr 0.01 * $i] "$cbr_($i) start"
    $ns_ at $val(simtime) "$node_($i) reset";
}
$ns_ at $val(simtime) "stop"
$ns_ at $val(simtime).01 "puts \"NS EXITING...\" ; $ns_ halt"
proc stop {} {
    global ns_ tracefd
    $ns_ flush-trace
    close $tracefd
}

puts "Starting Simulation..."
$ns_ run